UNIVERSITY OF IOANNINA
Department of Computer Science and Engineering

Virtual Labs 2:
“Fading Processes-Channel Characterization”
Documentation

Referring to Courses:
Wireless Links
of
Computer Science and Engineering
at
University of Ioannina

Prepared by
Priftis Filippo and Prifti Joanis
at
Computer Science and Engineering
at
University of Ioannina

Portability
This project may execute in every operating system that supports octave.

Project Structure
FIRST_GUI.m: This function file acts as “main” function. It calls all the functions needed for the simulation to run. First it calls the show_FIRST_GUI function which initializes GUI.Then it calls realCarSimulator function which we will describe shortly.
FIRST_GUI_def.m:This function file includes functions that initialize the main GUI components as well as the callback function(The function called every time that a user interacts with a gui component e.g a button) for every component.
realCarSimulator.m:This function generates the real world environment of the experiment i.e the buildings, the road,the car and the antenna.It also simulates the movement of the car and the change of the buildings width and the antenna’s height as well.
showReport.m: This function creates the report figures that occurs after simulation’s end.
(Under Construction!)
jakes.m: The jakes fading signal creation method.
pulses.m: creates a signal of N smoothed pulses, emulating the shadowing imposed by the
buildings.
berfading.m:This function was used as it is from matlab. It has some modification so that it works properly on octave. Yet this function is not fully implemented and has some errors that need to be handled.
 smooth.m: This function was also used as it is from matlab. It has no differences compared to the original matlab function.
 ricepdf.m: Rice/Rician probability density function (pdf).
TVLABS2CustomMeasurement.m: Custom TMeasurement for internal use in the VLABs2.
Functions are modified to return the Gains of the receiving antenna Gr, the transmitting
antenna Gs and the space loss L.

Ροή προγράμματος
Αρχικά, η εκτέλεση της εφαρμογής ξεκινάει από την συνάρτηση FIRST_GUI(βρίσκεται στο FIRST_GUI.m) η οποία με την σειρά της καλεί την συνάρτηση FIRST_GUI_def(βρίσκεται στο FIRST_GUI_def.m) ώστε να εμφανιστεί το κυρίως παράθυρο της εφαρμογής με τις επιλογές παραμετροποίησης του πειράματος καθώς και το παράθυρο με το αυτοκίνητο.
Τα γραφικά στοιχεία του κυρίως παραθύρου αρχικοποιούνται στην συνάρτηση show_FIRST_GUI() με την μορφή struct το καθένα.
Στο κυρίως παράθυρο μπορούν να δωθούν τιμές για το πείραμα από τους αντίστοιχους sliders όπως επίσης και τα drop down menus . Για τους sliders και τα πεδία αυτά υπάρχουν αντίστοιχα για το καθένα μία συνάρτηση(callback, δηλαδή που εκτελείται κάθε φορά που ο χρήστης αλληλεπιδρά με το στοιχείο του γραφικού περιβάλλοντος) που είναι υπεύθυνη να παίρνει την τιμή αυτή και να ενημερώνει επίσης και το αντίστοιχο label στα αριστερά ώστε να μπορεί να βλέπει ο χρήστης την τιμή που έχει ο slider εκείνη την στιγμή όπως επίσης και την μονάδα μέτρησης. Οι συναρτήσεις αυτές είναι της μορφής GUIcomponent_doIt().
Στην συνέχεια ο χρήστης μπορεί να παραμετροποιήσει τα πεδία της κεραίας που είναι επιλεγμένη εκείνη τη στιγμή στο drop down menu πατώντας το κουμπί Edit. Μόλις πατηθεί το κουμπί αυτό καλείται η συνάρτηση TransmitAndReceiv_Edit_doIt() η οποία ελέγχει ποιος τύπος κεραίας είναι επιλεγμένος εκείνη την στιγμή και καλεί με την σειρά της την συνάρτηση setFigContext() η οποία καθορίζει το ή τα πεδία της αντίστοιχης κεραίας και εμφανίζει ένα νέο παράθυρο με αυτά τα πεδία. Με παρόμοιο τρόπο λειτουργεί το Edit στο Medium panel με την διαφορά ότι η συνάρτηση που καλείται είναι η Medium_Edit_doIt() που με την σειρά της καλεί την setPropagationModel() η οποία καθορίζει τα αντίστοιχα πεδία και τα εμφανίζει αντίστοιχα σε ένα παράθυρο.
Σημαντική παρατήρηση(TODO): Όσον αφορά τα πεδία που εμφανίζονται πατώντας τα αντίστοιχα κουμπιά Edit δεν τα χρησιμοποιούμε κάπου ενώ θα έπρεπε ώστε να γίνει σωστά η προσομοίωση.